## Slide 1
Smart
Companion
PicoBot
Your Smart Reminder, Your Health Partner
Medicine
Reminder
Voice
Assistant
Face
Reaction
Movement
Detection
Emergency
SMS
01
Presented by: Adika Sultana-23101162
Medicine
Robot

## Slide 2
Executive Summary
02
1
Why We Built It
Many elderly and chronically ill patients forget their medicine, and many skip it on purpose. Reminder apps only fight forgetting, and caregivers cannot always be present. We built PicoBot to close this gap.
2
Our Goal
Raise medication adherence with a low-cost companion robot that tackles both forgetting and unwillingness, and keeps the user safe with an instant emergency SMS alert.
3
My Contribution
50% Literature Gap · 50% Survey · Problem Statement · Why This Topic · Conceptual Model · Hardware & Budget · Fully Circuit Design · 50% Hardware Implementation · Gantt Chart · Video
75%
of 28 older adults want daily medication reminders [15]
79%
want emergency assistance from a caregiving AI [15]
2
causes of non-adherence: forgetting and unwillingness
Tk 4,236
total cost of the PicoBot prototype

## Slide 3
My Contribution
03
✓
Literature Gap
Read 2 papers and built the literature gap from them.
✓
Survey
50% of the survey is done, based on the literature gap.
✓
Problem Statement
Forgetting, refusal, no confirmation and absent caregivers.
✓
Why This Topic
Most tools fix only forgetting; we join robotics, AI voice and IoT.
✓
Conceptual Model
Forgetting: reminder + confirmation. Unwillingness: emotional engagement.
✓
Circuit Design
ESP32-S3 wiring for all modules and power.
✓
Video
Project video showing how PicoBot works.
✓
Gantt Chart
12-week plan; the last 2 weeks are for the paper and report.
✓
Hardware & Budget
15 components selected, total cost tk 4,236.
✓
Hardware Implementation
Wired MQ-2, PIR, touch, voltage divider, I2S amplifier, buck converter and capacitor.

## Slide 4
Problem Statement
Many elderly or chronically ill patients simply forget medicine timing, dosage, or whether they already took it.
Even when reminded, many skip medicine on purpose low mood, denial, or simply not feeling like it.
Reminder apps only fight forgetting they can't sense reluctance or confirm the dose was truly taken.
Caregivers can't always be present, leaving emergencies or emotional low points without easily accessible help.
04

## Slide 5
Why We Choose This
Topic?
Non-adherence has two causes forgetting and unwillingness yet most tools fix only the first.
Combines robotics, AI voice, affective computing, and IoT to address both memory and motivation.
Supports independent living and emotional well-being, not just pill-time alerts.
Backed by recent adherence and social-robotics research scalable, research-grounded design.
05

## Slide 6
Literature Gap
06
Study | Reminder & Confirmation | Emotional Refusal | Safety Net | Limitation
Tamantini et al. (2025) [14] Virtual agent that switches between enthusiastic and neutral style from the user’s facial emotion (20 participants) | Not addressed Questionnaire task, not medicine | Yes Adapts speaking style to the user’s emotion | Not addressed | Not medicine-specific; needs a camera and GPT-4; no significant experience gain over a static form
Wolfe et al. (2025) [15] Mixed-method study of older adults’ views on caregiving AI chatbots (medication reminders, companionship) | Interest only 75% (21/28) want daily medication reminders | Partly Users split into adapters, wary and resisters | Interest only 79% (22/28) want emergency assistance | Attitude study, not a built system; usability barriers remain for older adults
PicoBot (Ours) Reminder + persuasion + emergency alert in one low-cost ESP32-S3 robot | Yes RTC alarm, voice, button confirmation | Yes Empathetic voice + mood-aware face | Yes MQ-2 gas alert, SMS, SD log | Prototype stage field evaluation is proposed future work

## Slide 7
Survey Analysis
Q1 · Respondent Background
What is your relationship to the intended user of the robot?
Chart: 
| Patient (user) | Family / caregiver | Healthcare professional | Technology evaluator
Share of responses (%) | 47.4 | 13.2 | 7.9 | 31.6
38 responses
Q2 · Respondent Background
How often does the intended user forget to take medicine on time?
Chart: 
| Rarely | Occasionally | Frequently | Almost daily
Share of responses (%) | 13.5 | 43.2 | 8.1 | 35.1
37 responses
Q3 · Reminder & Alert Design
Which reminder method would be most effective for the user?
Chart: 
| Voice alert only | Voice + facial expression | Voice + phone notification | Simple sound alarm
Share of responses (%) | 55.3 | 13.2 | 15.8 | 15.8
38 responses
07

## Slide 8
Survey Analysis
Q4 · Reminder & Alert Design
If the first reminder is ignored, how should the robot respond?
Chart: 
| Repeat every 2-3 min | Gradually increase volume | Notify caregiver after one miss | Wait, then escalate to caregiver
Share of responses (%) | 11.1 | 36.1 | 22.2 | 30.6
36 responses
Q5 · Reminder & Alert Design
How long should the robot keep reminding before a dose is logged as missed?
Chart: 
| 5 minutes | 15 minutes | 30 minutes
Share of responses (%) | 5.3 | 50 | 44.7
38 responses
Q6 · Emotional Engagement
How useful would a facial expression feature be for the user?
Chart: 
| Very useful | Somewhat useful | Not useful
Share of responses (%) | 53.1 | 34.4 | 12.5
32 responses
08

## Slide 9
Survey Analysis
09
Q7 · Emotional Engagement
When the user shows reluctance, what robot response is most appropriate?
Chart: 
| Empathetic verbal encouragement | Firm, direct reminder | Alert a caregiver
Share of responses (%) | 81.5 | 11.1 | 7.4
27 responses
Q8 · Emotional Engagement
What tone of voice would be most acceptable for spoken reminders?
Chart: 
| Warm and friendly | Calm and formal | Neutral, robotic
Share of responses (%) | 60.7 | 21.4 | 17.9
28 responses
Q9 · Safety & Monitoring
How important is the movement / presence detection feature?
Chart: 
| Essential | Important | Optional | Not important
Share of responses (%) | 69 | 3.4 | 3.4 | 24.1
29 responses

## Slide 10
Concept Model: Solving Both Sides of Non-Adherence
10
Forgetting
Wrong time, wrong dose, or no memory of taking it at all
Unwillingness
Low mood, denial, or simply not feeling like it today
Reminder + Confirmation
Voice alarm, RTC schedule, persistent alerts until the button is pressed
Emotional Engagement
Empathetic voice persuasion and mood-aware facial expressions
Smart Medicine Companion Robot
Medicine Actually Taken
Caregiver Peace of Mind
Emergency Safety Net

## Slide 11
Hardware Components
ESP32-S3-WROOM-1 (N16R8)
0.96″ I2C OLED Display
HC-SR501 PIR Sensor
DS3231 RTC (ZS-042)
MAX98357A I2S Amplifier
3W 8Ω Speaker
KY-040 Rotary Encoder
MQ-2 Gas Sensor
TTP223 Touch Module
SIM800L GSM Module
MP1584 Buck Converter
1000 µF Capacitor
DC Jack
5V/3A Adapter
Resistors ×4 (SIM800L divider)
11

## Slide 12
Components Budget
12
1 | ESP32-S3-WROOM-1 (N16R8) Board | 1 | Tk 950
2 | KY-040 Rotary Encoder | 1 | Tk 110
3 | HC-SR501 PIR Sensor | 1 | Tk 95
4 | TTP223 Touch Module | 1 | Tk 40
5 | 0.96″ I2C OLED Display | 1 | Tk 350
6 | DS3231 RTC Module (ZS-042) | 1 | Tk 345
7 | MQ-2 Gas Sensor Module | 1 | Tk 160
8 | SIM800L GSM Module | 1 | Tk 650
9 | MAX98357A I2S Amplifier | 1 | Tk 601
10 | 3 W, 8 Ω Speaker | 1 | Tk 450
11 | MP1584 Buck Converter | 1 | Tk 90
12 | 1000 µF Capacitor | 1 | Tk 15
13 | DC Jack | 1 | Tk 20
14 | 5 V / 3 A Adapter | 1 | Tk 350
15 | Resistors (SIM800L divider) | 4 | Tk 10
 | Total |  | Tk 4,236

## Slide 13
Robot Circuit Diagram
13

## Slide 14
Hardware Implementation
MQ-2 Gas Sensor
Emergency SMS
detects gas leaks in the room and triggers the alert
PIR Sensor
Movement Detection
senses user presence and engages automatically
Touch Module
Persistent Alarm
user touches to confirm medicine taken and stop it
Buck Converter
Power Supply
steps the 5V/3A adapter down to a steady supply for every module
Voltage Divider
Safe Input Level
two resistors scale the MQ-2 output down for the ESP32-S3
I2S Amplifier
Voice Reminder MAX98357A drives the 3 W speaker for spoken reminders
1000 µF Capacitor
Power Filtering
smooths voltage spikes so the modules stay stable
14

## Slide 15
Project Timeline: Gantt Chart
15
Task
W1
W2
W3
W4
W5
W6
W7
W8
W9
W10
W11
W12
1. Literature review & survey
3 wk
2. Problem statement & objectives
2 wk
3. Concept model & system design
3 wk
4. Component selection & procurement
2 wk
5. Circuit design & wiring
2 wk
6. Reminder module: RTC, voice, button
3 wk
7. Emotional engagement: OLED face, persuasion
3 wk
8. Presence (PIR) & gas-leak SMS alert
3 wk
9. Integration, SD logging & enclosure
2 wk
10. Testing & refinement
5 wk
11. Paper & report
2 wk
Phases:
Plan
Design
Build
Test & Report

## Slide 16
Conclusion
The Smart Medicine Companion Robot is a compact, intelligent, and interactive solution for medicine management.
It improves medication adherence, ensures safety, and brings peace of mind to users and caregivers.
It combines robotics, IoT, voice interaction, and emotional engagement in one platform.
This project has strong potential to make a real-world impact in healthcare.
“Technology with Care, Health Everywhere.”
16
Project Demonstration

## Slide 17
Our Reference Papers
Adapting Virtual Agent Interaction Style with Reinforcement Learning to Enhance Affective Engagement
Frontiers in Digital Health
Tamantini, C., Umbrico, A., Fracasso, F., Beraldo, G., Cortellessa, G., & Orlandini, A. (2025)
Link: https://doi.org/10.3389/fdgth.2025.1680605
Caregiving Artificial Intelligence Chatbot for Older Adults and Their Preferences, Well-Being, and Social Connectivity: Mixed-Method Study
Journal of Medical Internet Research, 27, e65776
Wolfe, B. H., Oh, Y. J., Choung, H., Cui, X., Weinzapfel, J., Cooper, R. A., Lee, H.-N., & Lehto, R. (2025)
Link: https://doi.org/10.2196/65776
17

## Slide 18
Thank You For Your Attention
18